## Slide 1: Drive system for an electric Go-kart
Group 841

## Slide 2: Introduction
Group PED 841
Faheem Ahmad
Nicolas Murguizur Bustos
Aitor Teran
Mihai Rusu
Nicolai Fransen
Estefania Ruiz

## Slide 3: Agenda
Motivation & objectives
Hardware
Control
Firmware
Test results
Conclusion
Demonstration

## Slide 4: Motivation
Slide
of 59
Mihai
Develop a control algorithm for the power train of an electrical go-kart
Objectives
Design and simulation
Implement FOC in a digital signal processor (DSP)
Interface board
Inverter tests
Modelling the battery pack
Experimental setup
Project management

## Slide 5: Hardware
Notes: Motivation
Existing problems
What is a MIC
Why a MIC
Problem statement

## Slide 6: TSA170-210-038 Sauer Danfoss
Slide
of 59
Induction machine nominal parameters |  | 
Power | Pn | 5.3 [kW]
Phase voltage | Un | 13.85 [V]
Phase current | In | 189 [A]
Power factor | PF | 0.76
Stator frequency | fn | 58 [Hz]
Mechanical shaft speed | ωn | 1685 [rpm]
Electromagnetic torque | Tn | 30.04 [Nm]
Mihai

## Slide 7: Batteries
Mihai

## Slide 8: Batteries – obtaining parameters
Why short pulse test?
Points of interest
Goal
Mihai

## Slide 9: Batteries – experimental parameters
Battery | Rated capacity | Charging capacity | Discharging capacity | Efficiency
A | 55Ah | 14.4Ah | 14.4Ah | 80%
B | 55Ah | 35Ah | 33Ah | 94.2%
D | 55Ah | 19.3Ah | 17.7Ah | 91.7%
Battery | Rs’ (datasheet) | Rs’ | Rt | 
A | 2mΩ | 10mΩ | 24mΩ | 205s
B | 2mΩ | 7mΩ | 22mΩ | 205s
D | 2mΩ | 8mΩ | 22mΩ | 205s
Battery | Rs’ (datasheet) | Rs’ | Rt | 
A | 2mΩ | 10mΩ | 24mΩ | 205s
B | 2mΩ | 7mΩ | 22mΩ | 205s
D | 2mΩ | 8mΩ | 22mΩ | 205s
Mihai

## Slide 10: Batteries – SOC vs. VOC curve
Mihai
Observations
How is obtained?

## Slide 11: Batteries – simulation result
Observations
Is it satisfactory?
What can be improved?
Mihai

## Slide 12: Interface Board
Slide
of 59
Sections of board
Power supply
DSP development kit
Reference selection
Faheem

## Slide 13: Inverter
Slide
of 59
Inverter Electrical Characteristics
Power capability : 7.3kW
DC link voltage : 36V
Switching frequency : 20kHz
MOSFET Used
Infineon OptiMOSTM : 80V 300A
Package type : PG-HSOF-8-1
Max. allowed Tj : 175℃
Faheem

## Slide 14: Inverter thermal test
Slide
of 59
Inverter case temperature test at different operating condition up to rated values
DC link voltage (V) | Average drain current (A) | Temp. (Thermocouple) (℃) | Temp. (Simulation) (℃)
12.5 | 55 | 24.8 | 26.8
18 | 100 | 28 | 30.3
24 | 152 | 37 | 36.7
33 | 172 | 44.8 | 40.3
38 | 190 | 50.5 | 43.8
Faheem

## Slide 15: Control of the induction machine

## Slide 16: Field Oriented Control (FOC)
Slide
of 59
Estefanía
Notes: FOC  field orientation in order to achieve independent control of the torque and rotor flux by controlling the stator currents in the dq- reference frame.
Necessary to perform reference frame transformation then the rotor flux field position is found from the rotor mechanical speed and the slip speed.
Two types of control  Torque control (2 PI controllers for torque - iq and flux - id) and Speed control (cascaded controller 3 PIs )
Modulation technique for controlling the gate signals of the VSI  SVPWM
- General block diagram of FOC where we have…..

## Slide 17: Space Vector Modulation PWM
Slide
of 59
Estefanía
Why SVPWM?
Better performance than SPWM
Output voltage can be increased up to 15%  Better use of
Lower THD  higher efficiency
Flexibility to be implemented digitally  DSP
Notes: Most popular SPWM but has drawbacks as high harmonic distortion
This technique allows to obtain a flattened voltage ref. waveform by reducing the peak voltage by approx 15% compared to fundamental.
Better utilization of Vdc without entering the overmodulation región  low THD
It is decided to select this modulation technique for controlling the VSC of this Project because of these advantages and its flexibility to…
Not mention overmodulation be concise dont explain too much.

## Slide 18: Rotor flux oriented control
Slide
of 59
Estefanía
Alternate form
Notes: Basic idea is to use an arbitrary dq frame where rotor flux is constantly aligned with d-axis as shown on the diagram.
This orientation allows decoupling of the IM torque and flux control variables making it possible to operate the induction machine as a separately excited DC motor.
The general torque equation for an induction machine in the dq frame depends on both iqs and ids however, with FOC by forcing the rotor flux to be in the d-axis rotsting at synchronous speed the q-axis rotor flux becomes zero tghen obtaining the torque as a function of the q-axis current only.
Large Font size in final equation and change kt for k.
The torque is proportional to the q axis current keeping the flux constant!

## Slide 19: Rotor flux oriented control
Slide
of 59
Estefanía
Determination of rotor flux position
0
0
Slip speed ()
Notes: - 2 different ways of implementing FOC for determining the rotor flux position. Depending on the possibility to measure the rotor shaft position of the IM or not, direct or indirect FOC can be implemented. Indirect FOC  Encoder
From the rotor voltage eq of the IM it is obtained that for rotor flux oriented control the terms containing the rotor flux in the q axis disappear and the difference between the synchronous speed w_e and the shaft’s electrical speed is known as slip speed.
To obtain the rotor flux position the slip speed needs to be estimated from the IM equations. It’s obtained that it is a function of the stator currents in the dq fr.
Explain a bit slower the slip part because I was too fast.

## Slide 20: Rotor flux oriented control
Slide
of 59
Estefanía
Determination of rotor flux position
Notes: Once the slip speed is estimated, by adding to this speed the rotor speed obtained from the Encoder attached to the shaft, it’s posible to obtain the rotor flux position by integrating the total sum of the speeds.

## Slide 21: Rotor flux oriented control
Slide
of 59
Estefanía
Determination of
IM rated parameters:
From the IM equations:
Constant :
Notes: From the nameplate of the induction machine the rated voltage and current is obtained to calculate the stator flux linkage. Then the rated rotor flux linkage is calculated in order to obtain the reference for the d-axis current. The IM will perform as expected up to the rated speed which is around 1600rpm. After that point it would be necessary to weaken the flux in order to keep having a proper control of the IM. The motor will opérate in the field weakening región but this isnt scope od the Project.

## Slide 22: PI current controllers
Slide
of 59
Estefanía
Same PI parameters for and
Zero-pole cancellation method:
Overshoot < 2%
Notes: - The transfer function is the same for the d- and q-axis which means that the current loops for both will be exactly the same.
- The delay appears in the system because of the digital implementation in a microcontroller. The time for sampling the measured signals in the Analog to
Digital Converter (ADC) and the time it takes to perform the control algorithm have to be taken into account. The time delay was reduced as much as possible while programming the microcontroller achieving a total time delay of half a switching period (Td 0.5Ts).
The requirement fot the controller is that the bandwidth should be 500Hz then applying the zero-pole cancellatio nmethod, which consist on placing the controllers zero to cancel the plant’s pole, the Ki is obtain as a fiunction of motor parameters and Kp.

## Slide 23: PI current controllers
Slide
of 59
Estefanía

## Slide 24: PI speed controller
Slide
of 59
Estefanía
Zero-pole cancellation method:
(from step response)
Overshoot < 5%
Notes: - The outer speed loop is governed by the mechanical equation of the induction machine
The closed loop transfer function of the current controller can be reduced to a first order transfer function because the outer speed loop is much slower than the inner loop.
Following the same zero-pole cancellation technique, as done during the design of the current PI controllers, the zero is selected to cancel the induction machine’s pole.

## Slide 25: PI speed controller
Slide
of 59
Estefanía

## Slide 26: Simulation result
Slide
of 59
Torque Control

## Slide 27: Simulation result
Slide
of 59
Speed Control

## Slide 28: Regenerative braking
Slide
of 59
Negative slip
Negative torque
Faheem
When the rotor speed is higher than synchronous speed (i.e., negative slip), the machine runs in generation mode

## Slide 29: Regenerative braking simulation
Slide
of 59
Motor stops following torque reference during speed control
Downhill slope of 10°
Speed Control Region
Torque Control Region
Negative DC link Current
Both in torque control & speed control

## Slide 30
Firmware
Notes: Motivation
Existing problems
What is a MIC
Why a MIC
Problem statement

## Slide 31: Firmware Design
Slide
of 59
System feature definition
High level design
Low level design
Modular design
Allows collaboration between several developers
Increases scalability
Increases reliability
Allows code reusability
Nicolás

## Slide 32: High level design
Slide
of 59
For every software module
What is its goal?
When should the task be performed?
How will it interact with other modules?
Goal
Understand the big picture of the system
Nicolás
Unified Modeling Language (UML)

## Slide 33: High level design - Timing
Slide
of 59
Real time system: Time constraints
Motor control: calculation of new duty cycle every switching period
Other modules  Scheduler
Scheduler
Critical module
Calls tasks with different cyclicity
Nicolás

## Slide 34: Low level design
Slide
of 59
For every software module
Detailed explanation of module
Suggested data types, algorithms or patterns
Goal
Find technical limitations of the system
Speed up the development phase
Nicolás

## Slide 35: System
Slide
of 59
System are those modules which provide a framework for other modules
System Manager System supervision
Scheduler Task timing framework
Logger Debugging framework
Nicolás

## Slide 36: System manager
Slide
of 59
Features
System status
User interaction
Nicolás

## Slide 37: User interface
Slide
of 59
Different sources
Interface PCB
Graphical User Interface
Go-kart pedal
Reference Handler
Nicolás

## Slide 38: Motor control
Position estimation
Analog signal acquisition
Closed loop algorithm
Slide
of 59
Nicolai

## Slide 39: Position estimation
Slide
of 59
Nicolai
Notes: Calculate position from amount of pulses received
Calculate speed from the position change every 30 electrical degrees or within a specified time period (If speed is slow)
Slip speed is estimated from Machine parameters and dq-current references
Rotor flux speed is found by adding the shaft speed and the slip speed.
Integrated to optain estimated flux position, used for reference frame transformations

## Slide 40: Analog signal acquisition
Analog signal structure
  Raw ADC value
  Filtered value
  Previous value
  Filter order
  Filter frequency
  Filter parameters
  ADC channel
  Priority
  Safety thresholds
Interface functions
Slide
of 59
Nicolai

## Slide 41: Closed loop control algorithm
Slide
of 59
Nicolai
50µs

## Slide 42: Safety
Monitors possible error sources
  Overvoltage
  Overcurrent
  Temperatures
Performs the necessary safety reaction
Includes a watchdog timer
Slide
of 59
Nicolai

## Slide 43: System tests

## Slide 44: Test setup
Slide
of 59
Nicolai

## Slide 45: Load difference
Go-kart load
Load motor
Aitor
Notes: Simulation results are also different.
Mechanical model is completely different, which affects speed load but not torque reference due to similar RL load.
Mention PI parameters are different than in simulation.

## Slide 46: Torque control - Startup
Aitor

## Slide 47
Torque control – Load change
Aitor
Notes: Explain the change on speed in the right

## Slide 48: Speed control
Speed variation
Load variation
Aitor
Notes: Do not say real life, say tests, experimental…
Speed control is not quick, it’s actually slow.
Also talk about inertia here.
Not say actually and oscillations, more overshoot.
Steps of 25 or 50.

## Slide 49: Torque to speed transition
Simulation
Tests
Aitor
Notes: PI error is zero at the beginning and so torque ref goes down to zero, inertia helps stabilizing.
GENERAL: Overview slide in the beginning.

## Slide 50: Future work
Alternative approach in field oriented control
Implementation of regenerative braking
Performance at higher switching frequency
Integrating the power train in the go-kart platform
Picture of Go-kart here?
Aitor
Notes: Add arrows.

## Slide 51: Conclusions
Positive outcome
Simulation to implementation
Project management
Aitor
Notes: Add technical conclusions.
Change for arrows.

## Slide 52: Thank you for your attention
Questions?
Notes: Add technical conclusions.
Change for arrows.