## Slide 1: Parallel MOSFET
Slide
of 59
Using the motor power factor and efficiency we can calculate total apparent power
For a balanced 3-phase system
For a star connected load
Faheem
Drain
Source
Rgate
Rgate
Driver
DC Link
1
3
5
4
6
2
VA
VB
VC

## Slide 2: Parallel MOSFET
Slide
of 59
Faheem
By comparing multiple available MOSFETs from different manufactures of rating 60V and 80V for 300A.
Based on the obtained SPICE model simulation IPT007N06N and IPT012N08N5 are the most suitable MOSFETS. But, due to IPT012N08N5 higher drain-source voltage of 80V, it can ensure a better safety margin that occurs in turn off transition of the MOSFETs.

## Slide 3: MOSFET loss calculation
Slide
of 59
Faheem
Operating Condition |  | 
 | Values | Unit
DC link voltage (VDC) | 36 | V
Power Rating | 7.3 | kW
RMS current (IRMS) | 263 | A
Peak current (Ipk) | 371 | A
Switching Frequency (fsw) | 20 | kHz
MOSFET Parameter (IPT012N08N5) |  | 
 | Values | Unit
DS voltage (VDS) | 80 | V
RDS(on),max | 1.2 | mΩ
Drain current (ID) | 300 | A
Output Capacitance (Qoss) | 208 | nC
Gate Capacitance (QG) | 178 | nC
MOSFET loss can be modelled in parts
Conduction losses
Switching losses
Gate loss